## Slide 1
Cycling Infrastructure's Impact on Road Safety In London
Group 4:
Albright Besung
Amandeep Singh
Hardik Sangwan
Laura Gamba R.
Manuella C. de Paulo
Soki Kimura

## Slide 2
Managing London's Conflicting Goals of Vision Zero & Cycling Growth
Data Sources:
TfL Road Safety Data
TfL Cycling Infrastructure
  Mayor's Transport Strategy Target: 65% reduction in people killed or seriously injured by 2022 compared to 2005-09
  2022 Position: 38% reduction.
Vision Zero London: The Mayor's Transport Strategy goal is to eliminate all deaths and severe injuries (KSIs) on London's transport system by 2041.
Limitations: There is limited historical data on:
-Cycling Infrastructure Changes
-Speed Limit Changes
-Traffic Flow at different speed limits
London Cycling Action Plan: Increase cycling levels to benefit public health
  Target: 1.3 million cycling trips by 2024
  2022 Position: 1.2 million cycling trips
Key Issue: Increasing cycling trips show a positive correlation with fatal and severe injuries (KSIs) over a 6-year period from 2017-2022
Notes: https://content.tfl.gov.uk/travel-in-london-2023-active-travel-trends-acc.pdf
https://www.sciencedirect.com/science/article/pii/S2214140518301488

## Slide 3
Summary: Accelerate Cycling Infrastructure Expansion to Reduce KSI while increasing cycling trips
Conducting a spatial analysis at the Borough Level for Pre- /Post- implemenation shows:
  Areas with improvement in cycle lane networks, like Barking and Dagenham, experienced notably lower Incident rates.
  Areas with less improvement in infrastructure, like Wandsworth and Croydon, experienced notably higher Incident rates.
Cycling infrastructure development has a negative correlation with fatal/serious injury incidents.
Incident distribution across London Boroughs highlights the need for continued investments in cycling infrastructure to create safer roads and urban environments.
Recommendations
Increase the rate of cycling infrastructure implementation to keep up with the growth in cycling trips so that Vision Zero Goals can be achieved in tandem.
Improve cycling infrastructure to bolster road safety in high-incident areas.
Regular assessments and improved data collection are needed to target further infrastructure improvements to mitigate risks.
Notes: Increase cycling infrastructure - road safety = negative correlation

## Slide 4
Areas committed to improving cycling infrastructure show improved traffic safety compared to pre- and post-implementation.
Waltham Forest ranked 5th for active travel. Its LTN improves walking & cycling, cutting casualties by ~50%. Similar success seen in other boroughs with LTNs
Barking and Dagenham implemented a 'Walking & Cycling Strategy' after being the second worst for road casualties.
Croydon: Sole London borough with no funding bids for enhancing cycle infrastructure.
Lowest proportion of LTNs.
Wandsworth Cycleways in Clapham junction see inadequate maintenance
Graphical Summary

## Slide 5
Additional Graphs and Calculations
Notes for TFL: Additional Data Requests for Time-series Analysis
Historical data for estimation of traffic across different speed limits.
The implementation date for cycleways, cycle parking, hiring station, LTN, school street, and other infrastructure-related data.
Temporal Analysis Issues:
Data for Infrastructure changes over time is unavailable. Only a spatial analysis of the relationship with safety is possible.
Regression Results:
Dependent Var: KSI, Independent Var: Cycling Hires: Relationship Coefficient (0.00013), p-value (<0.001), R-squared (0.31).
Future Research Questions:
Create a Multi-variate regression model analysing additional factors and strategies used by TfL for improving road safety.

## Slide 6: Casualties by Area
All KSIs per million vehicle miles for all transport modes
Cyclist casualties by cycling traffic density

## Slide 7
References and other resources
Barking and Dagenham - https://ehq-production-europe.s3.eu-west-1.amazonaws.com/ded4c1601ec4a70b6d2b654637dc3ab373c1c87a/original/1639580941/e685f2d629e13efbca152a4fab272d83_T2_LBBD_Outline_Walking___Cycling_Strategy_-_August__2021_Update.pdf?X-Amz-Algorithm=AWS4-HMAC-SHA256&X-Amz-Credential=AKIA4KKNQAKICO37GBEP%2F20240222%2Feu-west-1%2Fs3%2Faws4_request&X-Amz-Date=20240222T191633Z&X-Amz-Expires=300&X-Amz-SignedHeaders=host&X-Amz-Signature=03f5c7a7c44ed9931b898ffd710b61f9326d17f18a65680f9ff215cf5b9c7c8a
Croydon - https://www.mylondon.news/news/south-london-news/croydon-council-accused-showing-no-28631833
CUSP Data Dive Group 4 GitHub repo - https://github.com/sokimura39/CUSP_Data_Dive
https://findingspress.org/article/18330-the-impact-of-introducing-low-traffic-neighbourhoods-on-road-traffic-injuries LTN in boroughs to promote cycling are seen to have an impact on the road casualties
Marshall, W. and Ferenchak, N. 2019. Why cities with high bicycling rates are safer for all road users. Journal of Transport & Health. 13. Available from: https://doi.org/10.1016/j.jth.2019.03.004.
TFL- https://tfl.gov.uk/info-for/media/press-releases/2023/december/new-tfl-data-shows-sustained-increases-in-walking-and-cycling-in-the-capital#:~:text=The%20new%20data%20shows%20that,20%20per%20cent%20since%202019.
Waltham forest - https://www.walthamforest.gov.uk/media/4706
Wandsworth - https://www.cjag.org/2023/10/02/making-wandsworth-a-cycling-friendly-borough-is-there-enough-ambition/

## Slide 8: Other Factors Analysed
Traffic Changes – Observations hold when accounting for traffic fluctuations (looking at per mile travelled)
Policing – No statistically significant relationship found with KSI over 2017-2022
Speed Limit Reductions – Model was inaccurate without better data for estimating traffic flow rates through different speed limits over time
Safety Improvements in Buses and HGVs – Controlled by removing that mode of travel from the analysis subset

## Slide 9
Additional Graphs and Calculations
Notes for TFL: Additional Data Requests for Time-series analysis
Historical data for estimation of traffic across different speed limits
The implementation date for cycleways, cycle parking, hiring station, LTN, school street, and other infrastructure-related data
Temporal Analysis Issues:
Data for Infrastructure changes over time is unavailable. Only a spatial analysis of the relationship with safety is possible.
Regression Results:
Dependent Var: KSI, Independent Var: Cycling Hires: Relationship Coefficient (0.00013), p-value (<0.001), R-squared (0.31)
Future Research Questions:
Create a Multi-variate regression model analysing additional factors and strategies used by TfL for improving road safety

## Slide 10: Questions 1) Why have you chosen Croydon or Waltham Forest in particular? Ans) We choose these boroughs to show clear comparison, as boroughs like waltham and barking invested heavily in cycling infrastructure and we can clearly see less casualties there in contrast to their counterparts i.e Croydon or wandsworth. 2) Number of casualties have gone down in accordance with speed limit from 2016 to 2022 but speed limit casualties in 20km/hr have gone up. Can you explain that? Ans)With introduction of more 20km/hr road strips more vehicles are prompted to drive in 20-30 km/hr speed limit, this increase in speed limit causality is associated with that. 3) What do you think london should do to achieve its goals? Ans)As, we have said in our presentation, focusing more on a holistic approach of building better cycling infrastructure and cycling trips rather than just focusing increasing cycling trips could help in lowering cycling incidents.
4) You recommend increasing and improving cycling infrastructure to achieve better road safety, but your graph correlates increasing bike hires to higher KSIs trends.
Ans.: With better cycling infrastructure, there's a tendency of more people to start to cycle – hence more accidents might happen. Nevertheless, overall road casualties tend to decrease, as shown in papers of the literature (Marshall and Ferenchak, 2019).